## Slide 1
Electromagnetic Calorimeter (ECAL) 75848 crystals of lead tungstate (PbWO4 – 86% metal but completely transparent) are used to measure precisely the energies of electrons and photons in the barrel and endcaps of CMS. In the barrel the crystals are 2.2 x 2.2 x 23 cm3 and in the endcaps they are 3 x 3 x 22 cm3. A preshower detector, based on 4288 silicon sensors, each measuring 6.1 x 6.1 x 0.03 cm3, helps particle identification in the endcaps.
Preshower silicon sensor
Lead tungstate, before and after cutting and polishing
Barrel ECAL
Endcap Preshower
Endcap ECAL
How does the ECAL work?
How was the ECAL built?
Incoming electron/photon
Light detector
PbWO4 Crystal
Incoming electrons and
photons release all of their energy in
the PbWO4 crystals, producing a shower of particles as they do so. Light is also produced in the shower and measured by photodetectors (avalanche photodiodes – APDs – in the barrel; vacuum phototriodes – VPTs – in the endcaps) glued to the ends of the crystals; the amount of light is proportional to the energy of the electron/photon: more energy = more light.
Growing a PbWO4 crystal
takes about two days
After cutting and polishing,
all crystals are characterized
Photodetectors are glued
to the crystals and inserted
into support structures
Electronics, monitoring, safety and cooling systems are added
 Ready for installation
Up to 1700 crystals are grouped together
Silicon sensors for the
Preshower being wire-bonded
to readout electronics
A half-disc of the preshower ready for installation
Electromagnetic Calorimeter
(ECAL)
1)
2)
3)
4)
5)
7)
8)
5x5 groups of crystals being mounted on an endcap
6)